William Kinsey Moore
11/29/07
EE382
Term Project
Note: All graphs are attached and referenced as “Graph #” which appears at the top of the page containing the graphs in question. All calculations are attached on notebook paper, are referenced as “Calculations #”, and are labeled as such at the top of the page. Also attached are the pieces of Matlab code required to complete this project. They are referenced by and labeled “Matlab #”.
Part 1:
As seen in Graph 1, it takes the pulse at least 99 harmonics to converge, possibly more to reproduce the pulse in the required level of detail while it takes only 9 harmonics to approximate the sawtooth pattern accurately which is seen in Graph 2. The pulse takes more terms to converge than the sawtooth pattern, because the pulse has a large amount of frequency content at its discontinuities while the sawtooth has no discontinuities.
The end result of the calculations on Calculations 1 for the pulse is:
1 - e-jnπ
-2jnπ

The end result of the calculations on Calculations 2 for the sawtooth pattern is:
1 . (1 - e-jnπ)2
2 (jnπ)2
The Matlab functions that were used to generate these plots are contained in Matlab 1 and Matlab 2 and were generated by passing an arbitrary array into the functions as the t-axis and the number of harmonics required to be in the output.
Part 2:
The filter transfer function as calculated on Calculations 3 is:
H(ω) = (1+RCjω)-1
The filter utilizing the 1K ohm resistor removes some of the higher frequency content of the signals as they pass through it as observed in Graph 3 and Graph 4. When the 10K ohm resistor is used, the filter removes even more frequency content is removed as seen in the bottom halves of Graph 3 and Graph 4. The Matlab functions used to generate these graphs are contained in Matlab 3 and Matlab 4 using the t-axis values, the number of harmonics required, and the value of the resistor present in the filter as arguments.
Part 3:
The laplace transforms of the aperiodic waveforms are calculated and displayed on Calculations 3 and are labeled as Part 3.a and Part 3.b. The filter's laplace transform follows.
H(s) = (1+sRC)-1
The impulse response can be seen in Graph 5 and the two filtered aperiodic signals can be seen in Graph 6 and Graph 7. As show in Graph 6 and Graph 7, much of the frequency component is removed when the aperiodic signals are passed through the 1K ohm resistor filter.